SPRING COMMISSIONING YOUR NT

This checklist was designed to cover spring commissioning for my 37’ Nordic Tug for the first time and was also based on commissioning my previous 32’ Nordic Tug for several years.  It is meant to be as complete as possible so that I do not miss a critical item.  If you see any omissions please e-mail me at senojev@aol.com and I will update the Checklist.  Feel free to modify the Checklist to suit your needs.  Even if you do not do the work yourself, it is a good tool to check that required work is adequately specified and performed.

| Checklist Item | Complete |
| --- | --- |
| Inventory |  |
| Check Parts List versus inventory and replenish |  |
| Check fluid inventory and replenish |  |
| Check Tool Inventory and replenish |  |
| Documentation |  |
| Check current Registration Certificate (boat and dinghy), Registration decals, Registration numbers, Insurance Policy, Boat US membership, Certificate of Documentation, radio license. |  |
| Nav Rules, State Rules, Charts, Coast Pilot, Ports Guide, etc. |  |
| Boat and equipment manuals |  |
| Exterior |  |
| Clean fiberglass, buff as needed, polish and wax |  |
| Touch up any gel coat nicks |  |
| Polish and wax stainless steel |  |
| Clean boot stripe |  |
| Touch-up bottom paint |  |
| Clean and check prop |  |
| Check cutless bearing |  |
| Clean and check rudder |  |
| Clean and check rudder |  |
| Check paddlewheel |  |
| Check thru hulls |  |
| Clean vents |  |
| Check “zincs” (rudder, shaft, stern, bow thruster) |  |
| Check bow thruster prop and oil level, check electrical terminations are tight |  |
| Check engine room intakes for obstructions |  |
| Check antennae and wiring |  |
| Check fasteners for radar, TV and other pilothouse roof attachments |  |
| Check pilothouse to salon joint caulking |  |
| Check flag staff, davits, rails, ladders |  |
| Check sealing of all external attachments |  |
| Check function of wipers and washers |  |
| Top up washer fluid |  |
| Clean/polish/Rain-X outside of windows |  |
| Silicon window and screen tracks |  |
| Clean wiper blades, replace as necessary |  |
| Lube padlocks and door locks |  |
| Clean/wax nonskid |  |
| Silicon forward, pilothouse and lazarette hatch gaskets, storage locker gaskets and deck fill o-rings |  |
| Inspect anchors, verify shackles seized and secure (primary and secondary) |  |
| Check condition of rode/chain splice |  |
| Verify chain/rode depth markings are clear |  |
| Check shore mooring lines |  |
| Check mooring bridle and chain snubber |  |
| Check function of windlass from forward and from helm |  |
| Inspect dock lines, wash as necessary |  |
| Check fenders and inflate |  |
| Inspect shore power cables and adaptors |  |
| Lubricate any canvas zippers |  |
| Lazarette and Lockers |  |
| Clean out lazarette |  |
| Check bilge pump functions on auto and manual |  |
| Check seacocks and set postion |  |
| Check macerator seacock is disabled |  |
| Check hoses and fuel lines |  |
| Check hose clamps |  |
| Check steering gear fasteners and for any fluid leaks |  |
| Repack lazarette – make sure contents will not interfere with steering gear |  |
| Clean out stern storage locker and repack |  |
| Clean out propane locker and vent is clear |  |
| Check tank has gas and shows no corrosion |  |
| Check need for tank recertification |  |
| Check condition of hoses, clamps and function of solenoid valve |  |
| Dinghy and Outboard |  |
| Inflate dingy and check for leak and damage |  |
| Check tank and hoses for damage |  |
| Fill tank and add any additives used |  |
| Check outboard cut-off, oil, air filter, spark plug, lower unit, prop, grease |  |
| Check prop |  |
| Check davits |  |
| Check oars |  |
| Inside |  |
| Wipe over all interior surfaces |  |
| Clean/polish windows – Fog-X pilothouse windows |  |
| Clean screens |  |
| Vacuum blinds, carpet, drawers, cupboards, lockers |  |
| Check hoses and hose clamps in lockers |  |
| Exercise any seacocks and leave in preferred positions, check plugs are available |  |
| Oil teak |  |
| Wax shower walls |  |
| Clean toilet |  |
| Clean carpets |  |
| Make up beds |  |
| Provision |  |
| Shaft Alley |  |
| Clean out shaft alley and verify bilge pump works on auto and manual |  |
| Check PSS shaft seal and hose |  |
| Check integrity of fuel lines and function of valves – leave valves in preferred position |  |
| Inspect any other hoses especially water heater and hose clamps for tightness |  |
| Check and clean water pump strainers |  |
| Exercise any seacocks and leave in preferred position. Plugs available? |  |
| Polish fuel |  |
| Safety Equipment |  |
| Verify sufficient current day/night signals are onboard |  |
| Verify sufficient fire extinguishers are installed and pressurized. |  |
| Invert extinguishers to loosen contents |  |
| Verify installed fire extinguisher systems are pressurized and of correct weight (look at manual for specific requirements and records needed) |  |
| Verify sound signal and back-up work |  |
| Check navigation lights work |  |
| Check throwable device is available and undamaged |  |
| Check sufficient life jackets are onboard and in good condition |  |
| Check self inflating life jackets are armed and inflators are not expired |  |
| Change batteries in smoke and carbon monoxide detectors, verify function |  |
| Check first aid kit against inventory and expiration dates |  |
| Verify EPIRB battery is current for the season |  |
| Helm and Interior Electrics |  |
| Check steering fluid level |  |
| Power up AC panel, check breakers |  |
| Check outlets have power |  |
| Verify GFCIs trip |  |
| Check appliances |  |
| Apply power to DC panel and check breakers |  |
| Check DC outlets, lights, fans, and defrosters |  |
| Check bow thruster works |  |
| Check function of electronics/instruments/gauges to extent possible |  |
| Check and clean filters for A/C units |  |
| Charge any hand-held items such as VHF radios and GPS |  |
| Engine Room |  |
| Check oil/coolant levels in engine, generator, and transmission |  |
| Change oil/filters in engine, generator and transmission if not done at lay-up |  |
| Check engine zincs |  |
| Change fuel filters if not done at lay-up |  |
| Check all hoses and fuel lines for wear, damage and aging |  |
| Ensure all hose clamps are tight |  |
| Exercise all seacocks and fuel valves and leave in preferred position. Verify plugs are available for seacocks |  |
| Remove and clean raw water strainer baskets for engine/generator and A/C, inspect o-rings for damage and apply silicon grease to rings. |  |
| Inspect engine and generator belts for wear and correct tension |  |
| Inspect/replace raw water impellers |  |
| Check tightness of battery terminal connections and freedom from corrosion. Spray with anti-corrosion spray. Check hold-downs. |  |
| Check tightness of cables at chargers, inverters and other major equipment |  |
| Check electrolyte levels in flooded cell batteries and top up as necessary. |  |
| Charge batteries until fully charge and, after rest, check specific gravity is within specs for flooded cells |  |
| Replace any water filters |  |
| Inspect air filters (engine and generator) |  |
| Check engine room lights and outlets work |  |
| Replace bilge pump oil pads if needed |  |
| On the Water |  |
| Check for any leaks throughout boat |  |
| Sea trial |  |
| Full test of electronics |  |
| Test water heater |  |
| Test A/C and heaters |  |
| Before leaving boat, double check docklines and fenders, do any inspection for leaks and make sure bilge pumps are set to auto. |  |
| Additional Items |  |